## Slide 1: Artistic Stylization of Images and Video Part III – Anisotropy and Filtering Eurographics 2011
Jan Eric Kyprianidis
Hasso-Plattner-Institut, University of Potsdam, Germany

## Slide 2: Image/Video Abstraction
Stylized Augmented Reality for Improved Immersion
  Fischer et al., 2005
Real-time Video Abstraction
  Winnemöller et al., SIGGRAPH 2006
Coherent Line Drawings
  Kang et al., NPAR 2007
Structure Adaptive Image Abstraction
  Kyprianidis & Döllner, EG Theory and Practice of Computer Graphics 2008
Flow-based Image Abstraction
  Kang et al., Transactions on Visualization and Computer Graphics 2009
Artistic Edge and Corner Preserving Smoothing
  Papari et al., IEEE Transactions on Image Processing 2007
Image and Video Abstraction by Anisotropic Kuwahara Filtering
  Kyprianidis et al., Pacific Graphics 2009
Shape-simplifying Image Abstraction
  Kang & Lee, Pacific Graphics 2008
Image and Video Abstraction by Coherence-Enhancing Filtering
  Kyprianidis & Kang, Eurographics 2011

## Slide 3: Stylized Augmented Reality for Improved Immersion Fischer et al. (2005)
Non-photorealistic display of both the camera image and virtual objects:
Abstraction: Bilateral filter applied to Gaussian pyramid and then upsampled
Edges: Canny edge detector + morphological dilation
Conventional augmented reality
Stylized
augmented reality
Image credit: Fischer et. al. (2005)

## Slide 4: Real-time Video Abstraction Winnemöller et al. (2006)
Abstraction: Multiple iterations of xy-separable bilateral filter + color quantization
Edges: Difference of Gaussians + thresholding
Image credit: Winnemöller et. al. (2006)

## Slide 5: Coherent Line Drawings Kang et al. (2007)
Edges: 1D difference of Gaussians directed by flow field + flow-guided smoothing and thresholding.
Input image
Edge Tangent Flow
Line drawing
Flow-based filtering
Image credit: Kang et. al. (2007)

## Slide 6: Structure Adaptive Image Abstraction Kyprianidis & Döllner (2008)
Abstraction: Multiple iterations of orientation-aligned bilateral filter
Edges: separable flow-based difference of Gaussians
Local orientation and an anisotropy measure derived from the smoothed structure tensor are used to guide the bilateral and difference of Gaussians filters
Original photograph
copyright
Anthony Santella

## Slide 7: Flow-based Image Abstraction Kang et al. (2009)
Abstraction: Multiple iterations of flow-based bilateral filter
Edges: (separable) flow-based difference of Gaussians
Local orientation estimation of both techniques is based on the edge tangent flow (ETF)
Image credit: Kang et. al. (2009)

## Slide 8: Artistic Edge and Corner Preserving Smoothing Papari et al. (2009)
Generalization of the Kuwahara filter. Creates output with a painterly look.
Addresses two key issues of the original Kuwahara filter:
  Rectangular subregions
  Unstable subregion selection process
Credit for images: Papari et. al. (2009)

## Slide 9: Anisotropic Kuwahara Filtering Kyprianidis et al. (2009)
Further generalization of the Kuwahara filter.
Adaptation of the shape, scale and orientation of the filter to the local image structure.
Original image by Paulo Brandão@flickr.com

## Slide 10: Shape-simplifying Image Abstraction Kang & Lee (2008)
PDE-based technique that simultaneous simplifies colors and shape:
  Constrained mean curvature flow
  Shock filter
Input
60 iterations
40 iterations
20 iterations
Image credit: Kang & Lee (2008) / original image by Tambako the Jaguar@flickr.com

## Slide 11: Difference of Gaussians
Difference of Gaussians:
Laplacian of Gaussian (LoG)
Isotropic Difference of Gaussians (DoG)
Flow-based Difference of Gaussians
Separable Flow-based Difference of Gaussians

## Slide 12: DoG Edges vs Canny Edges
Isotropic difference of Gaussians
Canny Edges
Flow-based difference of Gaussians
Original image from USC-SIPI Image Database

## Slide 13: Edge Detection
Edge profile without noise:
Scanline of an image
First derivative
of scanline
Second derivative
of scanline
Edges are located at minima or maxima of the first derivative
Edges are located at zero crossings of the second derivative

## Slide 14: Edge Detection
Edge profile with noise:
Scanline of an image with noise
First derivative
of scanline
Second derivative
of scanline
First derivative sensitive
to noise
Second derivative even more sensitive
to noise

## Slide 15: Laplacian of Gaussian (LoG) Marr & Hildreth (1980)
In 2D the second derivative corresponds to the Laplacian:
Similar to the second derivative the Laplacian is sensitive to noise. To make the Laplacian less sensitive to noise, apply a Gaussian to the image first:
,
where is a 2D Gaussian with standard deviation :

## Slide 16: Difference of Gaussians (DoG) Marr & Hildreth (1980)
A Laplacian of Gaussian can be approximated by a difference of Gaussians:
Good engineering solution:
Fast to implement since Gaussian
is separable

## Slide 17: Difference of Gaussians (DoG) Marr & Hildreth (1980)
Zero-crossing are found by thresholding:

## Slide 18: Smooth DoG Edges Winnemöller et al. (2006)
An approach to created smooth edges was proposed by Winnemöller et al.:
The parameter controls the sensitivity to noise. A typical values are or .
The falloff parameter determines the sharpness of edge representations, typical values are .

## Slide 19: Smooth DoG Edges Winnemöller et al. (2006)
0
Edge
1
DoG
tanh
(half-truncated)
Credit for slide: H. Winnemöller

## Slide 20: Difference of Gaussians Guided by Local Image Structure
Local Structure Estimation:
Edge Tangent Flow
Structure Tensor
DoG Guided by Local Image Structure:
Flow-based DoG
Separable flow-based DoG
Original photograph
copyright
Anthony Santella

## Slide 21: Edge Tangent Flow Kang et al. (2007)
Edge Tangent Flow (ETF):
Smoothly varying vector field
Feature-preserving flow
Input image
ETF
Input image
Edge Tangent Flow
Image credit: Kang et al. (2007)

## Slide 22: Edge Tangent Flow Kang et al. (2007)
Weighted vector smoothing similar to bilateral filter:
is calculated using the
Sobel filter.
Multiple iterations (
Image credit: Kang et al. (2007)
ETF
Input image

## Slide 23: Edge Tangent Flow Kang et al. (2007)
Input image
ETF
Assure different vectors point in the same direction
Restrict filtering to a predefined radius
More weight to vectors with higher gradient magnitude
More weight for vectors with direction similar to current
filter origin

## Slide 24: Flow-based Difference of Gaussians Kang et al. (2007)
DoG filter
FDoG
response
Image credit: Kang et al. (2007)

## Slide 25: Structure Tensor
Let denote the input image and let
be the partial derivatives of .
The structure tensor is then defined by:
In differential geometry the structure tensor is also known as first fundamental form
The structure tensor is a symmetric positive semidefinte matrix
These can be implemented for example using Gaussian derivatives or the Sobel filter.

## Slide 26: Structure Tensor
The induced quadratic form of the structure tensor measures the squared rate of change of in direction of a vector :
The extremal values of on the unit circle correspond to the eigenvalues of :
The corresponding eigenvectors are:
Eigenvector of major eigenvalue. Direction of maximum change: gradient direction.
Eigenvector of minor eigenvalue. Direction of minimum change: tangent direction.

## Slide 27: Structure Tensor
The eigenvectors corresponding to the minor eigenvalues of the structure define a vector field. Typically this field is not smooth:

## Slide 28: Smoothed Structure Tensor
Smoothing the structure tensor prior to eigenanalysis with a Gaussian filter removes discontinuities in the vector field:

## Slide 29: Smoothed Structure Tensor
Eigenvector field of the smoothed structure tensor is similar to the edge tangent flow, but allows a more efficient implementation:
3 iterations of edge tangent flow filter
Eigenvector field of the smoothed
structure tensor

## Slide 30: Separable Flow-based Difference of Gaussians Kyprianidis & Döllner (2008)
Split flow-based difference of Gaussians into two passes:
1st Pass: one-dimensional DoG in direction of the major eigenvector
2nd Pass: smoothing along stream lines defined by minor eigenvector
1st Pass
2nd Pass

## Slide 31: Bilateral Filter
Bilateral Filter:
Classical Bilateral Filter
xy-Separable Bilateral Filter
Orientation-aligned Bilateral Filter
Flow-based Bilateral Filter

## Slide 32: Bilateral Filter Tomasi & Manduchi (1998)
More weight to closer pixel
More weight to pixel with
similar color
The bilateral filter is a nonlinear operation that smoothes images while preserving edges:

## Slide 33: Bilateral Filter Tomasi & Manduchi (1998)
The bilateral filter is a powerful tool, but computationally very expensive ( per pixel).

## Slide 34: xy-Separable Bilateral Filter Pham & van Vliet (2005)
1st Pass
2nd Pass

## Slide 35: xy-Separable Bilateral Filter Pham (2006)
Much faster than classical bilateral filter
But creates noticeable artifacts!
Full kernel bilateral filter
xy-separable bilateral filter

## Slide 36: Orientation-aligned Bilateral Filter Kyprianidis & Döllner (2008)
Align separable bilateral filter to local orientation derived from the smoothed structure tensor
1st Pass
2nd Pass

## Slide 37: Orientation-aligned Bilateral Filter Kyprianidis & Döllner (2008)
Less artifacts. Very well suited for abstraction.
Full kernel bilateral filter
Orientation-aligned bilateral filter

## Slide 38: Orientation-aligned Bilateral Filter Kyprianidis & Döllner (2008)
Linear smoothing of neighboring pixel values creates smooth color boundaries
Unit step size either along
x- or y-axis

## Slide 39: Flow-based Bilateral Filter Kang et al. (2009)
ETF-guided decomposition of bilateral filter
1st pass in direction of the tangent
2nd pass along stream line defined by
the ETF
Image credit: Kang et al. (2009)

## Slide 40: Flow-based Bilateral Filter Kang et al. (2009)
Excellent preservation of highly anisotropic image features
Input image
Bilateral filter
Flow-based bilateral filter
Image credit: Kang et al. (2009)

## Slide 41: Color Quantization Winnemöller et al. (2006)

## Slide 42: Color Quantization Winnemöller et al. (2006)
Apply quantization to luminance channel
Input
Result
Credit for slide: H. Winnemöller

## Slide 43: Color Quantization Winnemöller et al. (2006)
q0
q1
q2
…
Luminance
Q(.)
q
Luminance Mapping
q bins
tanh
per bin
Hard
Soft
Credit for slide: H. Winnemöller

## Slide 44: Color Quantization Winnemöller et al. (2006)
Abstracted
Sharp Quantization
(Toon-like)
Smooth Quantization
(Paint-like)
Image credit: Winnemöller et al. (2006)

## Slide 45: Kuwahara Filter
Kuwahara Filter:
Classical Kuwahara Filter
Kuwahara Filter with Weighting Functions
Generalized Kuwahara Filter
Anisotropic Kuwahara Filter
  Convolution-based Weighting Functions
  Polynomial Weighting Functions

## Slide 46: Kuwahara Filter

## Slide 47: Kuwahara Filter
For every subregion calculate the mean
and the variance:
The output of the Kuwahara filter is then defined as the mean of a subregion with minimum variance:

## Slide 48: Kuwahara Filter
Region with small variance. All pixels of this region are similar.
Regions with high variance. They all contain pixels from both color regions.
Result is the mean of the region with minimum variance
Kuwahara filter for a corner

## Slide 49: Kuwahara Filter
Region with small variance. All pixels of the region lie on the same side of the edge.
Regions with high variance. They all contain pixels from both sides of the edge.
Result is the mean of the region with minimum variance
Kuwahara filter for an edge

## Slide 50: Kuwahara Filter
All regions have similar variance!
Selection of the region with minimum variance is highly unstable. For example if noise is present.
Kuwahara filter for an homogenous neighborhood

## Slide 51: Kuwahara Filter
Original image by Keven Law@flickr.com

## Slide 52: Kuwahara Filter

## Slide 53: Kuwahara Filter with Weighting Functions

## Slide 54: Kuwahara Filter with Weighting Functions
Then the mean is given by:
And the variance is given by:

## Slide 55: Generalized Kuwahara Filter Papari et al. (2007)
...
Idea: Create smooth weighting functions over a disc those sum is a Gaussian

## Slide 56: Generalized Kuwahara Filter Weighting Function Construction

## Slide 57: Generalized Kuwahara Filter
Then the mean is given by:
And the variance is given by:
The output of the generalized Kuwahara Filter is now defined by:

## Slide 58: Generalized Kuwahara Filter
The parameter is a tuning parameter that controls the sharpness of color boundaries. A typical value is
Sectors with high variance:
(i.e. almost no
influence to sum)
Sectors low high variance:
(i.e. most influence
to sum)

## Slide 59: Generalized Kuwahara Filter
Sector with small variance. All pixels of this sector are similar. This sector contributes most to the final result
Sectors with high variance. They all contain pixels from both color regions. These sectors have almost no influence.
Generalized Kuwahara filter for a corner

## Slide 60: Generalized Kuwahara Filter
Multiple sectors with small variance. All pixels of the sectors lie on the same side of the edge. Result is a weighted sum of the (weighted) mean values of the sectors.
Regions with high variance. They all contain pixels from both sides of the edge. These sector have almost no influence.
Generalized Kuwahara filter for an edge
Filter shape is similar to a truncated Gaussian

## Slide 61: Generalized Kuwahara Filter
All regions have similar variance!
Filter shape is similar to a Gaussian filter
Generalized Kuwahara filter for an homogenous neighborhood

## Slide 62: Generalized Kuwahara Filter
Original image by Keven Law@flickr.com

## Slide 63: Generalized Kuwahara Filter

## Slide 64: Anisotropic Kuwahara Filter Kyprianidis et al. (2009)
...

## Slide 65: Anisotropic Kuwahara Filter Algorithm Overview

## Slide 66: Anisotropic Kuwahara Filter Filter Shape Definition
Elliptic filter shape (Pham, 2006)
Here, denotes the anisotropy measure derived from the structure tensor.
is a user parameter that controls the eccentricity of the ellipse. A typical choice is .

## Slide 67: Anisotropic Kuwahara Filter
Sector with small variance. All pixels of this sector are similar. This sector contributes most to the final result
Sectors with high variance. They all contain pixels from both color regions. These sectors have almost no influence.
Anisotropic Kuwahara filter for a corner
Filter shape is adapted per-pixel

## Slide 68: Anisotropic Kuwahara Filter
Multiple sectors with small variance. All pixels of the sectors lie on the same side of the edge. Result is a weighted sum of the (weighted) mean values of the sectors.
Regions with high variance. They all contain pixels from both sides of the edge. These sector have almost no influence.
Anisotropic Kuwahara filter for an edge
Filter shape is adapted to anisotropic image structure

## Slide 69: Anisotropic Kuwahara Filter
All regions have similar variance!
Filter shape is circular and similar to a Gaussian filter
Anisotropic Kuwahara filter for an homogenous neighborhood

## Slide 70: Anisotropic Kuwahara Filter
All regions have similar variance!
Filter shape is similar to a Gaussian filter
Anisotropic Kuwahara filter for a homogenous neighborhood

## Slide 71: Anisotropic Kuwahara Filter
Original image by Keven Law@flickr.com

## Slide 72: Anisotropic Kuwahara Filter

## Slide 73: Anisotropic Kuwahara Filter Polynomial Weighting Functions

## Slide 74: Shape-simplifying Image Abstraction Kang & Lee (2008)
Mean curvature flow (Alvarez et al., 1992):
+
+
-
-
Increasing the intensity here moves the level curve
Decreasing the intensity here moves the level curve
Curvature
Image gradient

## Slide 75: Shape-simplifying Image Abstraction Kang & Lee (2008)
Mean curvature flow
Input
20 iterations
60 iterations
Image credit: Kang & Lee (2008)

## Slide 76: Shape-simplifying Image Abstraction Kang & Lee (2008)
Shock filter (Osher and Rudin, 1990; Alvarez and Mazorra 1994):
In the influence zone of a maximum, the Laplacian is negative and, therefore,
a dilation is performed.
In the influence zone of a minimum,
the Laplacian  is positive, which results in an erosion.
Input
Influence zones
Output
Image credit: Kang & Lee (2008)

## Slide 77: Shape-simplifying Image Abstraction Kang & Lee (2008)

## Slide 78: Shape-simplifying Image Abstraction Kang & Lee (2008)
Image abstraction by mean curvature flow
Input
20 iterations
60 iterations
Image credit: Kang & Lee (2008)

## Slide 79: Shape-simplifying Image Abstraction Kang & Lee (2008)
Constrained mean curvature flow:
with
Edge tangent
flow (ETF)
Stop diffusion if grafient is not aligned to edge tangent flow (ETF)
Image gradient

## Slide 80: Shape-simplifying Image Abstraction Kang & Lee (2008)

## Slide 81: Shape-simplifying Image Abstraction Kang & Lee (2008)
Image abstraction by constrained mean curvature flow
Input
60 iterations image abstraction by MCF
60 iterations image abstraction by CMCF
Image credit: Kang & Lee (2008)